BME680 connected to Raspberry Pi

# 1. Background

This project is part of a number of projects to measure the air quality I run into BM680 sensor from Bosch, which can measure temperature, pressure, humidity and volatile organic compounds (VOC) gasses. The board is the Adafruit BME680 I2C/SPI

The board and sensor is documented and there is software available for Arduino. That said, as with other Bosch Sensor BME280, the calculations are cryptic, not explained and impossible to understand. The code just works or not. I have studied the supporting code and made a version for the Raspberry PI.

There is a pre-compiled library that can provide a IAQ (Indoor Air Quality) index. Unfortunately there is not a single definition of IAQ index in the world and this is just another one. BOSCH does not want to disclose the calculation but the description of BOSCH implementation is (as with their other code) cryptic and feels over engineered and way to difficult. I have decided to leave that for what it is and not implement it. See more in the chapter for more about VOC resistance reading.

Paul van Haastrecht
paulvha@hotmail.com
# 2. Board layout

Source : https://learn.adafruit.com/adafruit-bme680-humidity-temperature-barometic-pressure-voc-gas/overview

Power Pins:
- Vin - this is the power pin. Since the sensor chip uses 3 VDC, we have included a voltage regulator on board that will take 3-5VDC and safely convert it down. To power the board, give it the same power as the logic level of your microcontroller - e.g. for a 5V micro like Arduino, use 5V
- 3Vo - this is the 3.3V output from the voltage regulator, you can grab up to 100mA from this if you like
- GND - common ground for power and logic
SPI Logic pins:

All pins going into the breakout have level shifting circuitry to make them 3-5V logic level safe. Use whatever logic level is on Vin!
- SCK - This is the SPI Clock pin, its an input to the chip
- SDO - this is the Serial Data Out / Master In Slave Out pin, for data sent from the BMP183 to your processor
- SDI - this is the Serial Data In / Master Out Slave In pin, for data sent from your processor to the BME680
- CS - this is the Chip Select pin, drop it low to start an SPI transaction. Its an input to the chip
If you want to connect multiple BME680's to one microcontroller, have them share the SDI, SDO and SCK pins. Then assign each one a unique CS pin.
I2C Logic pins:
- SCK - this is also the I2C clock pin, connect to your microcontrollers I2C clock line.
- SDI - this is also the I2C data pin, connect to your microcontrollers I2C data line.
Leave the other pins disconnected
By default, the i2c address is 0x77. If you add a jumper from SDO to GND, the address will change to 0x76.
# 3. Software installation

As with many of my projects I make use of the BCM23008 library to control the IO. The reason is that it is faster and more flexible than the wiringPi (which makes use of the official kernel drivers) and provides direct control and insight, which I like.
## 3.1 BCM2835 library
Install latest from BCM2835 from : http://www.airspayce.com/mikem/bcm2835/

1. wget http://www.airspayce.com/mikem/bcm2835/bcm2835-1.56.tar.gz
2. tar -zxf bcm2835-1.56.tar.gz	// 1.56 was version number at the time of writing
3. cd bcm2835-1.56
4. ./configure
5. sudo make check
6. sudo make install

In order for this software to run you should NOT enable i2C in raspi-config to load the kernel drivers. It works directly on the hardware, but you’ll have to run program as root if you select hard-I2C

## 3.2 twowire library
Obtain the latest version from : https://github.com/paulvha/twowire

1. download the zip-file (clone or download / download zip-file) in the wanted directory
2. unzip twowire-master.zip (*1)
3. cd twowire-master
4. make install

*1) if you do not have unzip : sudo apt-get install zip unzip

## 3.3 BME680 software
Obtain the latest version from : https://github.com/paulvha/bme680

1. Download the zip-file (clone or download / download zip-file) in the wanted directory
2. unzip bme680-master.zip (*1)
3. cd bme680-master
4. create the executable : make
5. To run you have to be as sudo ./bme680m -h ….

In the software package you will find the following files

bme680_lib.cpp :
This is glue between user level and BME680 driver from Bosch. The driver is based on the original version written for the Arduino, but adjusted and extended to work on the Raspberry Pi. Some routines have been added, a number have been changed.

bme680m.cpp :
This is the user level program that will be discussed in detail in a next section.

rasp_BME680.h :
This is the header file for the BME680. It is based on the original version written for the Arduino, but adjusted and extended to work on the Raspberry Pi.

Bosch driver files

source : https://github.com/BoschSensortec/BME680_driver

BME680.c, BME680_defs.h, BME60.h
(make sure you have the latest !)

makefile :
script to compile the source and create an executable with the make command.

# 4. Sensor driver

The BME680 driver for the program is divided over multiple files.

The BME60_lib.cpp serves as the glue between the user program and the BOSCH API:

rasp_BME680 class is the connection between the user program and the BOSCH driver
The low level routines for the BOSCH driver to access I2C read/write, millis and delay

The BME680.c
This is the API / driver provided by Bosch. This will provide routines to set the parameters correctly, to read the data and perform calculations for the BME680. The API has a number of complex calculations to for the temperature, humidity, pressure and gas. These are IMPOSSIBLE to understand and nowhere explained what it really does. It depends on the BME60_lib.cpp for the low level communication with the device.

The temperature, humidity and pressure sensors look to be the same as the BM280. Running both BME280 and BME680 in parallel provides nearly similar values. The VOC resistance output from the BME680 needs a long time to stabilize.

There is a routine to read the altitude based on the pressure (either in meter or feet), but that was assuming the standard defined pressure at sea level. I have changed that so one can now provide that yourself (e.g. from different websites) and compare that the obtained local pressure.
I have added the calculation for dew-point.

# 5. BME680m program

The program it self has a number of big blocks

1. Initialize variables to default settings
2. parse parameters
3. Initialize hardware (BCM2835 + sensor)
4. Main-loop to provide output
5. closeout()

## 5.1 initialize variables
Default values for the different parameters are loaded and result variables reset. The defaults are hard coded, some based on the different Arduino.ino files and some adjusted based on expected usage.

## 5.2 parse parameters
The program has a rich set of command line option (see 5.6 in detail later) to change many default settings. This can either be input on the command line.

## 5.3 initialize hardware
The BCM2835 and sensor is initialized with the different parameters.

## 5.4 main loop
The program will loop for reading, either a fixed number of times or endless (depending on the parameter see 5.6). The output of can be defined with parameters (see 5.7) by the user and will be displayed on the screen, but also be saved to a file if the user wants that.

## 5.5 closeout
Either close with Control-C or it will count down the number loops. The BCM2835 reset to the standard values.

## 5.6 parameters allowed
Please make sure to check the data sheet BME680 for the exact impact of some of the parameters.

-F filter
Adjust the filter coefficient setting from the default 7 (middle). With this option the IIR filter can be set to reduce the impact of sudden changes (e.g. slamming door) on temperature and pressure. The higher the value, the better smoothing out changes, but the more samples are needed to get to the real, current value. No impact on humidity.

-H oversampling
Change the level of oversampling the humidity from level 8 (the highest x 16). The more oversampling the less noise on the results, but it takes longer.

-M pressure
Calculate the height of the current location in meters compared to sea level. This is based on the provided current pressure of a place nearby at sea level (from an external website) and than compared against the local pressure. Must be 6 digits (like 102310 for 1023.10)

-P oversampling
Change the level of oversampling the pressure from level 8 (the highest x 16). The heigher oversampling the less noise on the results, but it takes longer.

-T oversampling
Change the level of oversampling the temperature from level 16 (the highest x 16) to a lower level. The more oversampling the less noise on the results.

-C heater temperature
Set the expected heater temperature (max 400 °C). default is 300 °C.

-K heater warm-up time:
Set the time to reach the heater temperature (max 4032mS) . default 150mS.

Parameters for General

-B
This will trigger to output results without color on the screen.

-L count
This will change the default endless loop (0) to a number of loops for the main loop before exiting.

-D delay
This can change default delay of 5 seconds between readings.

-O string
This will allow flexible output formatting. See chapter 5.7.

-V level
This will enable progress/debug information. Level 1 is user program, level 2 includes driver debug messages.

-W filename
Append the displayed output to the file.

Parameters for I2C

-A address
The i2C address can be changed from the default 0x77 to 0x76.

-i
This will trigger the twowire library to use hardware I2C instead of software I2C ( *1)

-I #
This will change the default 100Khz i2C speed to a value between 1 (Khz) to 400 (Khz) (*2)

-s #
change the soft_I2C SDA from default (GPIO 2 / pin 3) to another GPIO.

-d #
change the soft_I2C SCL from default (GPIO 3 / pin 5) to another GPIO

Note :
*1	if you set as hard_I2C you must run the program as root/super user.
*2	if using soft_I2C the maximum speed will be 200Khz (even if you set higher)

## 5.7 output formatting
By default the temperature, humidity,pressure, height and resistance values are only output.

The user can (with the -O option) create their own output format :

BME680 results
T = temperature in celsius
H = humidity
P = pressure
M = height in meters (assumes that -M current pressure was applied else 1023mBar)
R = VOC resistance
D = Dew-point

Markup
\l include local time
\t include tab
\s include space
\, include comma
        \; include semicolon
\n include newline
\\\x include the character x (x can be any character, TRIPLE SLASH!!)

Example -O “\lctTP”, will result in :
  Tue Oct 16 20:18:34 2018 Temp: 21.53 Pressure: 1021.53

Example -O “\lct\nT\,H”, will result in :
  Tue Oct 16 20:19:50 2018
  Temp: 20.53, Humidity: 34.93

# 6. Volatile organic compounds: little value

The volatile organic compounds (VOC) resistance is of little to NO value in my opinion. There are number of reasons for me to make this statement:

## 6.1 Does it reach the right temperature ?
6.1.1. While there is a check that the requested temperature was reached within the warm-up time (I have made sure to check that this status bit is set !) when program just started, the resistance numbers start low and then increase overtime (minutes). This is also after the sensor has been through many hours of burn-in before. WHY ? It is not because the API is leveling out (it is reading the raw value). If the MOX temperature would have been reached it should read the correct value without ramp of minutes.

6.1.2. This program has a standard delay between readings of 5 seconds, after running for a hour the resistance showed around 250 – 300 K. If you now change the loop delay to 15 seconds (-D option), and restart immediately you will see that the reading never reaches the reading that number and fluctuates around 190K. Changing back to 5 seconds brings the 250 – 300K again after a while. NOW changing it to 1 second, the value of is becoming 450 – 460K. Changing back to 5 seconds… well you know that story.

6.1.3. Set the warm-up time instead of 150ms to 1000ms (-K option) delay 5 seconds, the VOC resistance increases to 650 – 700K. Now what the heck ??

WHY IS THAT ?

A logical reason is that the sensor does not reach the expected temperature before performing the read-out, even though the status bit indicate different. According to the data-sheet (page 19) : “In practice, approximately 20–30 ms are necessary for the heater to reach the intended target temperature”. REALLY ?? even basic tests shows that is not the case , why else a ramp when started ?
It is a common, known, issue with VOC sensors that they need time to warm-up, but as the BME680 only has a forced mode, instead of (say 20 min warm-up) it is a big challenge.

Is issue 6.1.2 because the longer you warm up, the higher the temperature and thus the resistance is higher as the gas is more influenced ? Then what is it that is being measured and is the value of the reading ?

There are a number of web-sites/forums that try to interpret these resistance numbers, but depending on delay between readings and warm-up times, these numbers are completely random and not comparable, not usable. The data-sheet should provide clear direction.

## 6.2 No explanation about resistance.
There is NO description on how resistance value relate to any of the potential gasses. (CO, CO2 etc) All of the other MOX/VOC sensors that I have worked on, have a chart that is showing sensor values relates to potential gasses. As such (even if it was stable) the BME680 VOC resistance reading is useless information.

## 6.3 Indoor Air Quality (IAQ) ?
This is defined in many ways.

Source : https://en.wikipedia.org/wiki/Indoor_air_quality

IAQ is known to affect the health, comfort and well-being of building occupants. IAQ can be affected by gases (including carbon monoxide, radon, volatile organic compounds), particulates, microbial contaminants (mold, bacteria), or any mass or energy stressor that can induce adverse health conditions

source : https://pdfs.semanticscholar.org/f95c/6199b6759cc4b50f8159cae52c04ffc7e20e.pdf

The quality of the air inside a building is affected by a variety of comfort, physical, chemical and biological factors. Factors influencing the indoor air quality of a room or building include:
•	Comfort issues (temperature, humidity)
•	Supply of fresh air to the building,
•	Accumulation of particulate, biological or chemical contaminants originating from within or outside the building.

That said, we could fill many pages with definitions but THERE IS NO SINGLE MEASUREMENT / CALCULATION OF A STANDARD.

Now one can hope that the Indoor Air Quality (IAQ) coming from the BSEC library, which is only available in pre-compiled format, would be of help. I have serious doubts. Having read many documents around the IAQ topic and there is mention of many gasses and other aspects, that can not be measured by a single sensor.

There are only multiple measurements and this BOSCH IAQ is another one to add to the list. Next to that it expects days (4 or 28 days) of gathering baseline data. WHY ? I would expect a calibrated sensor be able to compare to a known value of “clean-air” to it’s current environment. If that current environment is very dirty it can detect right-away and fine-tune overtime. Otherwise that dirty environment becomes the baseline and the IAQ will only indicate whether it became more or less dirty… but still dirty.

## 6.4 So what ?
If you plan to buy the BME680 for the VOC measurement capabilities… I can only say “think twice”. If you are only interested in a change in resistance, due to a change in air quality, it is a good device. However there are many other sensors around that provide better documentation and better insights. If you plan to buy for temperature, humidity or pressure the sensor is good.. as good as BME280.

# 7. A word on the twowire library

The BCM2835 chip provides I2C communication protocol from the hardware. However the clock stretching implementation is bad, leading to many issues with slave devices that depend on or use clock stretching to handle the requests. (e.g. CCS811, SCD30 ) This library can handle that.

This library for the Raspberry Pi can be instructed to use the standard (hardware) I2C communication OR use a software version that supports clock stretching on any of the GPIO pins. This also supports for you to run multiple I2C channels at the same time on different GPIO. To have low processor load and increase stability, the maximum speed that is supported for the soft_I2C is 200Khz. However for compatibility reasons a higher speed request (max. 400Khz) will be accepted, which can be executed by hardware I2C communication, but for software I2C the maximum executed will be around 200Khz.

Note : The BME680 does NOT use clock stretching however and can be used to run with the hardware I2C communicator without any problems.

software version :
advantage:
can run multiple I2C channels for different programs in parallel
flexible on GPIO’s to use
run as any user (does not need root permission)
supports proper clock-stretch

disadvantage:
generates some process load (although acceptable low)
quality of communication depending on total processor load
supports speeds up to max 200Khz

hardware version :
advantage
generates lower process load
less / no dependency on processor load from other programs
supports speeds up to max 400Khz

disadvantage
single channel
fixed GPIO’s ( 2 and 3)
must be root or super user.
No clock-stretch support
# Appendix 1: Schematics

https://learn.adafruit.com/adafruit-bme680-humidity-temperature-barometic-pressure-voc-gas/downloads